| Six – Lead Stepper Motor Hook-Up Diagram 23D and 34D Series |
| --- |
| Connection | Lead Wire Connection | Stepper Motor Lead Wire Color |
| 4 - Lead Bipolar Series MBC or MLP Driver Series Do Not Connect Do Not Connect | Phase 1 (A) Phase 3 (/A) Phase 2 (B) Phase 4 (/B) | Red Red/White Green (GRN) GRN/WHT Black (BLK) White (WHT) |
| 6 - Lead Unipolar BLD, TM Driver Series | Phase 1 Phase 3 Phase 2 Phase 4 Common Phase 1 & 3 Common Phase 2 & 4 | Red Red/WHT Green (GRN) GRN/WHT Black (BLK) White (WHT) |